VISSIM modelling screen prints.

(Screen print 1) Traffic did not adhere to the road intervention schemes.

Location shown- The Old Railway Gate House. Orsted propose the road hump is graded with one-way priority signage. In this illustration traffic has ignored priority signs and tried to pass at the old railway hump. This part of the road is very narrow and is impossible for two vehicles to pass each other. Vattenfall have not proposed any changes to this location and OPC wonders how cable delivery vehicles will cope with this hazard.

(Screen print 2) Location shown – The Street at the entrance to Docking Farm. Passing places to be constructed by Orsted (shown in green) unable to accommodate all traffic if there were several vehicles following each other.

Vattenfall have not proposed any changes to the road. The amount of existing traffic together with the Orsted volumes would make the Vattenfall ‘pilot vehicle’ approach unrealistic.

(Screen print 3) Abnormal load leaving Orsted Hornsea Three’s Main construction compound along ‘The Street’ to B1149. NOTE: - Traffic held on B1149 in both directions for well over 5 minutes, with significant highway safety implications [bottom of screen print]. Traffic tailing back in an easterly direction towards a hump back bridge where the stationary traffic will not be seen by approaching fast moving traffic. This is also the part of the road that Vattenfall propose NOT using HDD to cross it thus adding to disfunction and danger.